How to use a Dryer

# What is a dryer?

A dryer is a mechanical device or machine that removes the water from 
wet grains by forcing either ambient air or heated air through the grain bulk.

# Why is proper usage of a dryer important?

Any delay in drying of wet paddy leads to rapid deterioration of quality. 
A dryer that does not perform well or is operated in the wrong way can cause 
several problems:

Extended drying time due to inefficient air delivery or low temperature

Uneven drying of the grains due to uneven airflow or too high temperatures (batch dryers)

High fuel consumption due to ineffective air distribution or too high airflow rates

Low germination rate due to too high drying air temperatures

High number of broken grains due to mixing of dry with wet grains or moisture gradients

Fire hazard and danger of CO poisoning of operators from using unsafe burners

# How to Dry

For optimum drying apply proper pre-drying management and operate the dryer according to the manual.

## Before drying

Prevent any delay in drying after harvest. If you can not dry the paddy to the desired moisture content at least pre-dry to 18%, which is safe for temporary storage for up to two weeks.

Clean the grains before drying to avoid uneven drying and wet spots.

Do not mix grain with different moisture content to avoid cracking.

Read the operators manual of the dryer and familiarize yourself with the operation.

## Using the dryer

Load the dryer with wet paddy, consider minimum load and don’t overload.

With very wet paddy or when paddy lots with different moisture content are mixed aerate or circulate the grains for 15-30 minutes before turning the heater on for reduction of broken grains.

In a batch dryer with more than 30cm grain depth mix the grains at least once for more even drying.

Monitor grain temperature and moisture content to prevent excess temperatures and over-drying.

Dry paddy after harvest to 18% MC for storage up to two weeks.

Dry paddy for milling to 14%. Drying below 14% reduces weight and milling yield.

For 8-12 month storage dry to 13% or less, for long term storage exceeding 1 year to 9%.

# Text boxes

## Safety precautions

Always operate the dryer as described in the manual

Service burners or furnaces regularly to prevent fire hazards and excess CO produciton and have a fire extinguisher at hand

Make sure that fuel cut-of valves that disconnect the fuel supply in case of power cuts are functioning

Ensure proper ventilation of the working area to prevent CO poisoning.

# For more information contact
Agricultural Engineering Unit
IRRI, DAPO Box 7777, Metro Manila, Philippines
Tel.: (63-2) 580-5600, Fax.: (63-2) 580-5699
Email: 	M.Gummert@cgiar.org
	J.Rickman@cgiar.org

IRRI  International Rice Research Institute