Paddy Drying Systems

# What is drying?

Drying is the process of removing water from the grains to reach safe storage moisture content (MC).

# Why dry?

## Paddy is harvested wet

Rice is harvested at grain MC between 20 and 30% (wet basis).

## Dried paddy can be stored safely

Depending in the desired storage period there are different recommended moisture contents for safe storage.

| Storage period | Required MC | Potential problems at higher MC |
| --- | --- | --- |
| 2 to 3 weeks | 14 - 18% | Molds, discoloration, respiration loss |
| 8 to 12 months | 13% or less | Insect damage |
| More than 1 year | 9 % or less | Loss of viability |

## Wet paddy deteriorates quickly

|  | Delays in drying, incomplete drying or uneven drying will result in qualitative and quantitative losses including: |
| --- | --- |

Yellowing or discoloration caused by mold development and heat build-up from respiration

Reduced milling yields caused by high temperatures and re-wetting of grains

Loss of germination and vigor from grain respiration, mold and insect activities, or from exposure of grains to temperatures above 42ºC

Damage caused by insects that are more active at higher MC levels

# Traditional drying system

|  | Sun drying is the preferred drying method in Asia by spreading the grains under the sun. It has low cost but is labor intensive and control of grain temperature is difficult. |
| --- | --- |

# Mechanical drying systems

## In-store drying

|  | Paddy with MC below 18% can be slowly dried in storage bins using aeration with slightly pre-heated air. |
| --- | --- |

## Heated air drying

|  | Fixed Bed Batch Dryer For farmers, contractors, small rice mills, flexible in capacity and heat source but labor intensive. |
| --- | --- |
|  | Re-circulating Batch Dryer For rice mills and cooperatives with automatic operation and good quality. |
|  | Continuous Flow Dryer For commercial grain centers for large capacity drying. |

# Text boxes

# For more information contact

Agricultural Engineering Unit 
IRRI, DAPO Box 7777, Metro Manila, Philippines
Tel.: (63-2) 580-5600, Fax.: (63-2) 580-5699
Email: 	M.Gummert@cgiar.org
	J.Rickman@cgiar.org