Measuring Varietal Purity

# Why measure varietal purity?

For seed to be classified as “good or certified seed” it must be able to pass a seed certification standard which determines whether the seed is true to varietal type..

# How to measure varietal purity?

Measurements needed to determine varietal purity are the grain size and shape, 1000grain weight and the number of red grains in the sample

## Grain size and shape

The grain size and shape (length-width ratio) is a very stable varietal property that can be used to measure the varietal purity of a sample.  Comparing the length-width ratio of the sample with the published ratio for the variety indicates the varietal purity of the grain sample. Significant deviation indicates that the sample is impure – that is, it is either a different variety or a mixture of varieties

| Scale (Length) |
| --- |
| 1 | Extra long (more than 7.5 mm) |
| 3 | Long (6.6 to 7.5 mm) |
| 5 | Medium (5.51 to 6.6 mm) |
| 7 | Short (5.5mm or less) |

| Scale | Shape | Ratio |
| --- | --- | --- |
| 1 | Slender | Over 3.0 |
| 3 | Medium | 2.1 to 3.0 |
| 5 | Bold | 1.1 to 2.0 |
| 9 | Round | Less than 1.1 |

### Procedure

- Obtain a random sample from the seed batch.

- Collect twenty grains at random from this sample of seed

- Use a Vernier caliper or photographic enlarger to measure the dimensions of each of the twenty grains.

## 1000 grain weight.

Each variety has a published weight for 1000 grains. If the 1000-grain weight calculated from the sample departs from this, it may be an indication that the sample contains a mixture of varieties.

### Procedure

- Select a random sample from the seed batch

- Count 1,000 whole grains from the sample.

- Weigh the 1,000 grains.

## Red grains

A grain is considered to be red if more than 25% of its surface area is red colored or streaked.

Procedure

- Select a random sample of the milled rice. 25gm is a good sample size.

- Weigh the sample

- Select and separate the red grains from the sample. The red kernels are those that have 25% or more of the grain red as shown in the diagram below:

- Weigh the red grains separated from the sample

- Calculate the percentage of red grains in the sample using the formula:

# Text boxes

# For more information contact
Agricultural Engineering Unit
IRRI, DAPO Box 7777, Metro Manila, Philippines
Tel.: (63-2) 580-5600, Fax.: (63-2) 580-5699
Email: 	M.Gummert@cgiar.org
	J.Rickman@cgiar.org

IRRI  International Rice Research Institute